## Slide 1
Basics of Electronics Engineering
Presented By:
Dr. Gurjinder Singh
Chitkara University, Punjab, India

## Slide 2: Why was digital electronics needed??
□ Most analog systems were less accurate, and were slow in computation and performance.
Digital system have the ability to work faster than analog equivalents, and can operate on very high frequencies too ! ! ! ! !
It was much economical than analog methodologies as the performance was faster !

## Slide 3: What are Integrated Circuits (IC’s) ???
□ IC’s are the micro circuits which are fabricated on a very small silicon wafers (chip) at which various components like BJT, CMOS etc. are mounted up to make a wholesome functional unit.
□ These days, various types of circuit integrations are possible at large extent, i.e. small scale, large scale, and very large scale integration (VLSI).

## Slide 4: Number System
When we type some letters or words, the computer translates them in numbers as computers can understand only numbers.
A computer can understand the positional number system where there are only a few symbols called digits and these symbols represent different values depending on the position they occupy in the number.
The value of each digit in a number can be determined using −
The digit
The position of the digit in the number
The base of the number system (where the base is defined as the total number of digits available in the number system)

## Slide 5: Different Types of Number System

## Slide 6: Comparison between Different Number System

## Slide 7: Binary Number System
The binary number system is a numbering system that represents numeric values using two unique digits (0 and 1). Most computing devices use binary numbering to represent electronic circuit voltage state, (i.e., on/off switch), which considers 0 voltage input as off and 1 input as on.

## Slide 8: Binary Number Systems
All the information in the digital computer is represented as bit patterns
What is a bit pattern?
01010101 is called as the bit pattern
01010101
This is one bit

## Slide 9: Binary Number Systems
Look at this bit pattern
0101 0101
How many bits are present ?
Count the number of ones and the zeros in the above pattern

## Slide 10: Binary Number Systems
0101 0101 in the digital computer
Bit7 | Bit 6 | Bit 5 | Bit 4 | Bit 3 | Bit 2 | Bit 1 | Bit 0
0 (MSB) | 1 | 0 | 1 | 0 | 1 | 0 | 1 (LSB)
There are 8 bits in the above table
Group of 4 bits= 1 Nibble
Group of 8 bits= 1 Byte
Group of 16 bits = 1 Word
2 Bytes = 1 Word

## Slide 11: Binary Number Systems
A single bit can represent two states:0 1
Therefore, if you take two bits, you can use them to represent four unique states:
00, 01, 10, & 11
And, if you have three bits, then you can use them to represent eight unique states:
000, 001, 010, 011, 100, 101, 110, & 111

## Slide 12: Binary Number Systems
Bit7 | Bit 6 | Bit 5 | Bit 4 | Bit 3 | Bit 2 | Bit 1 | Bit 0
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
Bit positions and their values

## Slide 13
Binary Number Systems
Only two levels
Easy to represent binary values electrically
Can be implemented using circuits
Create the building blocks of modern computers

## Slide 14
  Binary is extremely simple to implement. Any system that has an "on" and "off" or "high" and "low" state can be used to encode and/or manipulate data.
  Binary is the lowest "base" possible (base 2) and hence any higher counting system can be easily encoded (e.g. decimal, octal, hexadecimal, etc.).
  Binary would be the most effective way to attempt to communicate with any type of alien civilization. Just as "math" is a type of universal language (any alien civilization would understand a sequence of prime numbers, for example) binary is a universal alphabet.
Advantages- Binary Numbers

## Slide 15: Convert Decimal to Binary
For Each Digit Position
Divide decimal number by the base (e.g. 2)
The remainder is the lowest-order digit
Repeat first two steps until no divisor remains.

## Slide 16: Convert Decimal to Binary
Example: Convert Decimal 13 (13 10) to Binary : Repeated division by 2 (till quotient is zero)
Divide-by -2 | Quotient | Remainder | Binary Bits
13/2 6 / 2 3 / 2 1 / 2 | 6 3 1 0 | 1 0 1 1 | Bit 0 = 1 Bit 1 = 0 Bit 3 = 1 Bit 4 = 1
Answer = 11012

## Slide 17: Convert Decimal to Binary (Fraction)
Example: Convert Decimal (.625 10) to Binary : Repeated multiplication by 2
Mult-by -2 | Ans | Carry | Binary Bits
.625 * 2 .250 * 2 0.50 * 2 0 * 2 | 1.250 0.50 1.00 0 | 1 0 1 - | 1 0 1 ---
Answer = .1012

## Slide 18: Convert Binary to Decimal Example: Convert 11012
Multiply each 1 bit by the appropriate power of 2 and add them together.
1
1
Bit 1
1
Bit 2
0
Bit 3
Bit 0

## Slide 19: Convert Binary to Decimal Example: Convert 11012
Bit7 | Bit 6 | Bit 5 | Bit 4 | Bit 3 | Bit 2 | Bit 1 | Bit 0
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
 |  |  |  | 1 | 1 | 0 | 1
Multiply with these values
8 x 1 + 4 x 1 + 2 x 0 + 1x 1 = 8 + 4 + 0 + 1
= 13

## Slide 20: Convert Binary to Decimal (Fraction) Example: Convert .11012
Bit -1 | Bit -2 | Bit -3 | Bit -4 | Bit -5 | Bit -6 |  | 
2-1 | 2-2 | 2-3 | 2-4 | 2-5 | 2-6 |  | 
0.5 | 0.25 | 0.125 | 0.062 | 1/32 | 1/64 |  | 
1 | 1 | 0 | 1 |  |  |  | 
Multiply with these values
0.5 x 1 + 0.25 x 1 + 0.125 x 0 + 0.062 x 1 = 0.5 + 0.25 + 0 + 0.062
= 0.8125

## Slide 21: Binary Number Systems
Example: 10112 or 1011 B
= 1 x 23 + 0 x 22 + 1 x 21 + 1 x 20
= 8 + 0 + 2 +1
= 1110

## Slide 22: Binary Number Systems
Example: 101102 or 10110 B
1 x 24+0 x 23 + 1 x 22 + 1 x 21 + 0 x 20
= 16 + 0 + 4 +2+0
= 2210

## Slide 23: Other Number Systems
Octal and hex are a convenient way to represent binary numbers, as used by computers.
Computer mechanics often need to write out binary quantities, but in practice writing out a binary number such as

## Slide 24: Other Number Systems
1001001101010001 is tedious, and prone to errors.
Therefore, binary quantities are written in a base-8 ("octal") or, much more commonly, a base-16 ("hexadecimal" or "hex") number format.

## Slide 25: Octal Number Systems
Base = 8 or ‘o’ or ‘Oct’
8 symbols: { 0, 1, 2, 3, 4, 5, 6, 7}
Example
123, 567, 7654 etc
987 This is incorrect why?
How to represent a Decimal Number using a Octal Number System ?

## Slide 26: Octal Number Systems (Decimal to Octal)
Repeated Division by 8
Example
21310 = ( )8 ?
Divide-by -8 | Quotient | Remainder | Octal digit
213 / 8 26 / 8 3 / 8 | 26 3 0 | 5 2 3 | Lower digit = 5 Second digit =2 Third digit =3
Answer = 3258

## Slide 27: Octal Number Systems (Decimal to Octal)
Convert 393 to octal
Divide-by -8 | Quotient | Remainder | Octal digit
393 / 8 49 / 8 6 / 8 | 49 6 0 | 1 1 6 | Lower digit = 1 Second digit =1 Third digit =6
Answer = 6118

## Slide 28: Convert Decimal to Octal (Fraction)
Example: Convert Decimal (.625 10) to Octal : Repeated multiplication by 8
Mult-by -8 | Ans | Carry | Number
.625 * 8 .00 * 8 | 5.00 00 | 5 0 | 
Answer = .508

## Slide 29: Octal Number Systems (Octal to Decimal)
How to convert 3258 back to Decimal ?
Use this table and multiply the digits with the position values
Digit 8 | Digit 7 | Digit 6 | Digit 5 | Digit 4 | Digit 3 | Digit 2 | Digit 1
87 | 86 | 85 | 84 | 83 | 82 | 81 | 80
…… | …… | 32768 | 4096 | 512 | 64 | 8 | 1

## Slide 30: Octal Number Systems (Octal to Decimal Example)
How to convert 3258 back to Decimal ?
Consider the above number
3 2 5 (8)
3 x 82 + 2 x 81 + 5 x 80 = 3 x 64 + 2 x 8 + 5 x 1
= 192 +16 + 5
= 213
Digit 1
Digit 2
Digit 3

## Slide 31: Octal Number Systems (Octal to Decimal Example)
Example Convert 6118
Consider the above number
6 1 1 (8)
6 x 82 + 1 x 81 + 1 x 80 = 6 x 64 + 1 x 8 + 1 x 1
= 384 + 8 + 1
= 393
Digit 1
Digit 2
Digit 3

## Slide 32
Octal Number Systems (Octal to Binary)
6 1 1 (8)
Write in combination of 2 bits
001
001
110
= 110 001 001

## Slide 33
Octal Number Systems (Binary to Octal)
Reverse the procedure
11011010101
Make combination of three bits, starting
From LSB
11 011 010 101
5
2
3
3
Answer :- 3325 (8)

## Slide 34: Hexadecimal Number Systems
Base = 16 or ‘H’ or ‘Hex’
16 symbols: { 0, 1, 2, 3, 4, 5, 6, 7,8,9 }
{ 10=A, 11=B, 12=C, 13=D, 14=E, 15= F}

## Slide 35: Hexadecimal Number Systems
{0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F} It uses 6
Letters !
Example AB12, 876F, FFFF etc
How to represent a Decimal Number using a Hexadecimal Number System ?

## Slide 36: Hex Number Systems (Decimal to Hexadecimal)
Repeated Division by 16
Example
21310 = ( )16 ?
Divide-by -16 | Quotient | Remainder | Hex digit
213 / 16 13 / 16 | 13 0 | 5 13 | Lower digit = 5 Second digit =D
Answer = D516

## Slide 37: Hex Number Systems (Hexadecimal to Decimal)
How to convert D516 back to Decimal ?
Use this table and multiply the digits with the position values
Digit 8 | Digit 7 | Digit 6 | Digit 5 | Digit 4 | Digit 3 | Digit 2 | Digit 1
167 | 166 | 165 | 164 | 163 | 162 | 161 | 160
…… | …… | ….. | …… | 4096 | 256 | 16 | 1

## Slide 38: Hex Number Systems
How to convert D516 back to Decimal ?
Consider the above number
D 5 (16)
Digit 2
D x 161 + 5 x 160 = 13 x 16 + 5 x 1
= 208 + 5
= 213
Digit 1

## Slide 39
Binary to Hexadecimal
Make combination of 4 bits
11011010101
Make combination of Four bits, starting
From LSB
110 1101 0101
5
D
6
Answer : 6D5 (16)

## Slide 40
Hexadecimal to Binary
Reverse the procedure and write
Equivalent bit in combination of 4 bits
2 A 6
0110
1010
0010
Answer :- 001010100110 (2)
2A6 (16)

## Slide 41
Octal to Hexadecimal
Convert Octal into Binary
Make combination of 4 bits
Write the equivalent Hexadecimal Number
Convert 24 (8) into ? (16)
24 (8) to Binary equivalent is
100
010
= 010100
Now make combinations of 4 bits
01 0100
4
1
Answer : 14 (16)

## Slide 42
Hexadecimal to Octal (Reverse the procedure)
Convert Hexadecimal into Binary
Make combination of 3 bits
Write the equivalent Octal Number
Convert 2A6 (16) into ? (8)
2 A 6 to Binary equivalent
1010
0010
= 001010100110
Now make combinations of 3 bits
001 010 100 110
6
4
Answer :- 1246 (8)
0110
2
1

## Slide 43
Summary
Decimal to any format :- Divide by the base, 2 for Binary, 8 for Octal and 16 for Hexa
Any format to Decimal :- Multiply by powers of base
Binary to Decimal 23 22 21 20
Octal to Decimal 83 82 81 80
Hexa to Decimal 163 162 161 160
Binary to Octal :- Combination of 3 bits
Octal to Binary :- Each digit into 3 bits
Binary to Hexa :- Combination of 4 bits
Hexa to Binary :- Each digit into 4 bits
Octal to Hexadecimal :- Octal to Binary to Hexadecimal
Hexadecimal to Octal :- Hexadecimal to Binary to Octal

## Slide 44
Remember the Binary Table

## Slide 45
Thank You